## Slide 1
Predict Air Pressure system failure
Rama Danda
DSC 680 - Summer 2021

## Slide 2: Domain Background
Predict Air Pressure systems(APS) failure used in Scania trucks
System is used for Braking and gear changes
Data set is readings from sensors in the system from everyday use
Positive and negative class if failure caused by APS or not

## Slide 3: Domain use case
Prevent maintenance checks not required
Reduce trucking business down time because of failure
Eliminate costly work required while hauling time bound deliveries

## Slide 4: Data sources
    Data sources is through UCI Machine Learning Repository
    Data source links:
    https://archive.ics.uci.edu/ml/datasets/APS+Failure+at+Scania+

## Slide 5: Defining the features & Target Variable
    171 features are numerical and histogram bins data and is anonymized for proprietary reasons
    Target label
      Positive class failure is due to component of the APS
      Negative class failure is not related to APS

## Slide 6: EDA
First graph EDA show Class distribution which is highly unbalanced dataset with positive and negative class.
Second graph show skewness to the left, while left tailed relative to the normally distributed from the kurtosis graph.

## Slide 7: EDA
Null validation EDA shows 80% missing and while other are close to 50% values missing.
Removed the top 10 features that has n/a values

## Slide 8: EDA
Density plots of the features ag_001 and ay_005 reveals the values of these two features lead to higher APS failure.
ee_005 and ba_004,cn_004,cs_004 has higher correlation to the class. ag_002, ag_001 & cn_000 has high degrees of failure in the APS

## Slide 9: Standardization & Transformation
MinMax Scalar transformation
SMOTE method to balance the data resulted in 33k -0’s and 16k -1’s

## Slide 10: Model building
F1 score as the measure to measure each model of
Logistic Regression
SGD Classifier
Decision Tree Classifier
AdaBoost

## Slide 11: Modeling & Results
Logistic Regression – 0.804
SGD Classifier – 0.768
Decision Tree Classifier – 0.777
AdaBoost – 0.84

## Slide 12: Model parameters
All the models are passed with the same set of 10-fold cross validation as a fixed
Parameter C is the hyper parameter used to combat the highly imbalanced dataset
Based on these three models, Adaboost with 0.84 F1 score performed best.

## Slide 13: Conclusion & next steps
Data cleansing and standardization
Expensive computations for building models
Build more models using Keras

## Slide 14: Acknowledgements & References:
1)Industrial Challenge: Using Machine Learning for Predicting Failures
  https://www.researchgate.net/publication/313065916_IDA_2016_Industrial_Challenge_Using_Machine_Learning_for_Predicting_Failures
2) Combining Boosted Trees with Metafeature Engineering for Predictive Maintenance
  https://repositorio.inesctec.pt/bitstream/123456789/4388/1/P-00K-WFP.pdf
3)Prediction of Failures in the Air Pressure System of Scania Trucks Using a Random Forest and Feature Engineering
  https://www.researchgate.net/publication/309195602_Prediction_of_Failures_in_the_Air_Pressure_System_of_Scania_Trucks_Using_a_Random_Forest_and_Feature_Engineering